## Slide 1: Emcomm and Digital Modes
Tuck Watkins, W6TUK
Michael Radovancevich, KI6JPH
Notes: <number>

## Slide 2: Emcomm Messages
Most messages are short, voice transmissions.
But what if you had to send:
A list of medicines that are needed at a hospital.
Directions to a specific incident location
A list of evacuees.
07/29/26
<number>
Notes: <number>

## Slide 3: Messaging Needs Vary
We are capable of supplying voice communications.
We can offer additional help.
Narrow Band Emergency Messaging System [NBEMS]
07/29/26
<number>
Notes: <number>

## Slide 4: NBEMS
Composed of three related programs:
Fldigi – Fast Light Digital Modem application
Flarq – Fast Light Automatic Repeat Request
Wrap – Embeds a checksum in a file
Download from www.w1hkj.com
Runs on Linux, Mac OSX, Windows
07/29/26
<number>
Notes: <number>

## Slide 5: What is a digital mode
Use the computer and a sound card to pass text or data over the air.
07/29/26
<number>
Notes: <number>

## Slide 6: What do you need?
A transceiver, e.g. an HT, Dual Band mobile, or HF capable radio.
Computer with a sound card
Cables.
Free software
We like using an external sound card
07/29/26
<number>
Notes: <number>

## Slide 7: How does it work?
You type text into a buffer in the computer
Then you hit the transmit button.
Computer encodes your text from 8-bit ASCII to another character code, e.g. varicode.
The encoded data is passed to a modulator
Then passed to your soundcard to produce audio.
Then to the radio and over the air.
07/29/26
<number>
Notes: <number>

## Slide 8: Why use these modes?
Reduced bandwidth.
Improved signal-to-noise performance.
Reduced transmitter power requirement.
Some modes also offer built-in automatic error correction.
Some are particularly good in adverse atmospherics.
Accurate transmission of long list of data.
07/29/26
<number>

## Slide 9: Some Examples
CW - Amplitude Shift Keying
MFSK – Multi-frequency Shift Keying
BPSK – Binary Phase Shift Keying
DominoEX - Multi-frequency Shift Keying
MT63 - Orthogonal Frequency Division Multiplexed
[These examples that follow come from ‘Sights and Sounds of Digital Signals’ at: www.w1hkj.com/FldigiHelp/Modes/index.htm]
07/29/26
<number>
Notes: <number>

## Slide 10: CW Sounds
20 WPM 100 WPM
07/29/26
<number>
From www.w1hkj.com/FldigiHelp/Modes/index.htm
Notes: <number>

## Slide 11: MFSK – Multi-frequency Shift Keying
Uses different frequencies to denote symbol change.
Techniques using concurrent and/or sequential tones that implement this mode.
Forward Error correction – very robust.
Requires accurate tuning.
Long path DX.
07/29/26
<number>
Notes: <number>

## Slide 12: MFSK - Sounds
MFSK 16 MFSK 32
07/29/26
<number>
Notes: <number>

## Slide 13: BPSK – Binary Phase Shift Keying
Commonly called PSK [Sometimes 2-PSK]
Relatively narrow bandwidth.
Good sensitivity to weak signals.
Use low power. Can be overdriven!
Forward Error Correction is not used.
There is a variant called Quarature Phase Shift Keying (QPSK) with error correction.
07/29/26
<number>
Notes: <number>

## Slide 14: BPSK – Sounds
BPSK 125 BPSK 250
07/29/26
<number>
Notes: <number>

## Slide 15: DominoEX
Single carrier with 18 tone frequency with constant phases.
Very robust, no FEC.
Good weak signal LF and high speed HF use
DominoEX 11 designed for NVIS (80m at night)
Tolerant of tuning issues. [up to 200Hz. offset]
07/29/26
<number>
Notes: <number>

## Slide 16: DominoEX - Sounds
DominoEX 11 DominoEX 22
07/29/26
<number>
Notes: <number>

## Slide 17: MT63
Orthogonal Frequency Division Multiplexed mode.
Highly redundant Forward Error Correction
Handles interference and fading well
Can be mistuned and still work [100 Hz]
A bit wider than other modes.
Stations must use same interleave settings.
07/29/26
<number>
Notes: <number>

## Slide 18: MT-63 Sounds
MT-63/500
MT63/2K
07/29/26
<number>

## Slide 19: Details
Mode | Symbol Rate (Baud) | Words per Minute | Bandwidth (Hz.)
CW | 10 | 20 | 50
CW | 50 | 100 | 200
MFSK-16 | 15.625 | 58 | 316
MFSK-32 | 31.200 | 120 | 630
BPSK-125 | 125 | 200 | 250
BPSK-250 | 250 | 400 | 500
MT63/500 | 5 | 50 | 500
MT63/2000 | 20 | 200 | 2000
DominoEx 11 | 10.766 | 80 | 262
DominoEx 22 | 21.533 | 160 | 524
07/29/26
<number>
From www.w1hkj.com/FldigiHelp/Modes/index.htm
Notes: <number>

## Slide 20: Fldigi Features
Supports a ten families of digital modes
Supports keyboard and file/mail exchanges.
Supports broadcast messages.
Supports Automatic Repeat Request (ARQ).
Implements optional Error Correction tools for files.
07/29/26
<number>

## Slide 21: Fldigi and Flarq
Flarq implements Automatic Repeat Request.
Message divided into small segments and sent from one station to another.
Each segment contains a checksum, a count of the bits in the segment.
Any segment received without the proper number of bits is re-requested.
Can be slow, but guarantees delivery.
07/29/26
<number>
Notes: <number>

## Slide 22: Fldigi and Wrap
Wrap allows recipient to verify transmission was received correctly.
Permits transmission to single or multiple stations. (Yes, broadcast transmissions!)
Checksum is embedded in the entire message to insure accurate message is sent.
MT63, MFSK, THOR or DOMINOEX recommended as the transfer protocol.
07/29/26
<number>

## Slide 23: Flarq vs Wrap
Flarq is used for station to station communication.
Message delivered is guaranteed correct.
This can be slow.
Wrap is used for broadcasting a message
It has a checksum to use in confirming the message received has no errors.
You have to re-request if checksum is wrong.
07/29/26
<number>

## Slide 24: Fldigi and NBEMS
NBEMS = Narrow Band Emergency Messaging System.
A suite advertising “error free transmission” of text, images and email files.
NBEMS is a specially packaged Windows version of flarq, and fldigi.
Designed for use with Outlook, Thunderbird, etc mail programs.
07/29/26
<number>
Notes: <number>

## Slide 25: Getting Started
Need a radio, a computer, a soundcard, and a way to cable them together.
We use computer cabled to SignaLink USB soundcard box cabled to our radios.
You can use internal soundcard in computer.
Software is free from www.w1hkj.com/
07/29/26
<number>
Notes: <number>

## Slide 26: Fldigi Setup
Review the Beginner’s Guide at Fldigi site.
Review the material on Installation at www.pa-sitrep.com/NBEMS/
If you use Windows be sure to follow the Calibration procedure at the pa-sitrep site.
You must configure: ‘Operator’ and ‘Sound Card’ [i.e. Audio] parameters.
Setting up ‘Rig Control’ is possible.
07/29/26
<number>
Notes: <number>

## Slide 27: Digital Mode Usage
Most soundcard digital modes use USB, never LSB.
Exceptions: Clover, RTTY, PACKET, AMTOR and PACTOR typically use LSB.
Don’t overdrive. Use less power, particularly locally.
07/29/26
<number>
Notes: <number>

## Slide 28: Where to Tune
At present no active nets on VHF or UHF.
2M FM 144.35, 145.03, 145.05 allocated for keyboard-to-keyboard.
2M SSB between 144.100 and 144.300.
[144.300 is FM, below that is SSB]
See band local plan at: www.n0ary.org/ncpa/
Also www.arrl.org/FandES/field/regulations/bandplan.html
07/29/26
<number>
Notes: <number>

## Slide 29: What now?
It is a promising technology for Emcomm.
It is sometimes awkward to use.
Has an active Emcomm user base. Atlantic Division using it. Particularly PA.
Popular among non-Emcomm HF users.
There is a learning curve. We need to address this.
07/29/26
<number>
Notes: <number>

## Slide 30: Notes
Digital mode technical descriptions: www.arrl.org/FandES/field/regulations/techchar/
Basic set up see Beginner’s Guide at fldigi site www.w1hkj.com
Further set up see www.pa-sitrep.com/NBEMS/
Calibrate Windows Sound cards: www.pa-sitrep.com/NBEMS/fldigi_calibration.htm
07/29/26
<number>